## Slide 1: CS 2160
Chapter 2
Instructions: Language of the Computer

## Slide 2: Instruction Set
The repertoire or “vocabulary” of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
Many modern computers also have simple instruction sets
  RISC (Reduced Instruction Set Computer)
§2.1 Introduction
62

## Slide 3: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E
64

## Slide 4
64

## Slide 5: Register Designations
register | Assembly name | comment
R0 | $zero | Always 0
R1 | $at | Reserved for assembler
R2-r3 | $v0-$v1 | Stores results
R4-r7 | $a0-$a3 | Stores arguments
R8-r15 | $t0-$t7 | Temporaries, not saved
R16-r23 | $s0-$s7 | Contents saved for use later
R24-r25 | $t8-$t9 | More temporaries, not saved
R26-r27 | $k0-$k1 | Reserved by operating system
R28 | $gp | Global pointer
R29 | $sp | Stack pointer
R30 | $fp | Frame pointer
r31 | $ra | Return address
64

## Slide 6: Arithmetic Example
C code:
f = (g + h) - (i + j);
MIPS assembly code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1
65
Not MIPS (fixed 3 slides later)

## Slide 7: Arithmetic Operations
Basic capability of every computer
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware
comment
Line of assembly code
65

## Slide 8: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register “file” or registers
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware
Not a file on disk
67

## Slide 9: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1
f
g
h
i
j
68

## Slide 10: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is “Bi” Endian
  MARS models little Endian
  Least significant byte at address of a word
  c.f. Big Endian: most-significant byte at least address (Motorola)
69

## Slide 11: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register
69

## Slide 12: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
70

## Slide 13: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!
We’re ignoring cache

## Slide 14: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction
72

## Slide 15: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero
72

## Slide 16: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers
73

## Slide 17: 2s-Complement Signed Integers
It’s how you represent negative integers
What’s -1?
  ….111111111111
  Add 1 to it, you get 0 (with an overflow)
General rule
  Flip 1’s to 0’s and 0’s to 1’s
  Add 1
Example: -4
Start with …00000100
…11111011 (flip bits
…11111100 (add 1)
74

## Slide 18: Why is…
Why is 1111 1111 1111 1111 1111 1111 1111 1111 (32 1’s) equal to -1?
Because if you add 1 to it, you get 0 (!)

## Slide 19: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
2n can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111
77

## Slide 20: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102
So if you add 2, it becomes 0
77

## Slide 21: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
78

## Slide 22: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
§2.5 Representing Instructions in the Computer
80

## Slide 23: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
25=32
82

## Slide 24: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Six fields
82

## Slide 25: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Four fields
lw $t0, 800($t1)
83

## Slide 26: I-Type Representations
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
lw $t0, 800($t1)
addi $t0, $t1, 8
Op rt, i(rs)
Op rt, rs, i
83

## Slide 27: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture
86

## Slide 28: Logical Operators
87
sll $t2,$s0,4 # reg $t2 = reg $s0 << 4 bits
Binary: 000000 00000 10000 01010 00100 000000
0000 0000 0001 0000 0101 0001 0000 0000
Hex: 0x00105100

## Slide 29: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
88

## Slide 30: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0
88

## Slide 31: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0
88

## Slide 32: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero
89

## Slide 33: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions
90

## Slide 34: How do BEQ/BNE Instructions Work?
Operation code for BEQ or BNE in bits 26-31
Registers to compare in bits 21-25 and 16-20
Jump-to offset in bits 0-15
  Signed integer (so ±32K)
  Number of instructions, not address locations
    Multiplied by 4
    Added to current program counter
op
rs
rt
Immediate Data
6 bits
5 bits
5 bits
16 bits
Instruction layout
0
31
90

## Slide 35: Note about the Program Counter
Shows the memory address from where the next instruction will be fetched
Therefore it is incremented as soon as an instruction is fetched
It does not point to the current instruction
Thus a branch offset of 0 does not reexecute the same instruction
  Which is what happens when the branch fails

## Slide 36: Program Counter Process
PC
Instruction
Memory
+4

## Slide 37: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, h, I, j… in $s0, $s1, $s2, $s3, $s4
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses
91

## Slide 38: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …
Multiplies i * 4
Location of save[i]
Increments i
92

## Slide 39: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks
93

## Slide 40: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt # set on less than
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L
93

## Slide 41: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions would take longer
beq and bne are the common case
This is a good design compromise
93

## Slide 42: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0
94

## Slide 43: Clever Use of SLTU
$t2 is the upper bound of an array
$s1 is the index into the array
Want to branch if $s1 is negative or $s1 > $t2
Sltu $t0, $s1, $t2
Beq $t0, $0, IndexOutOfBounds
$t0 is set if $s1 is positive and less than $t2
But not if $s1 is negative because most significant bit is set and so $s1 > $t2
95

## Slide 44: Procedure Calling
Steps required
  Place parameters in $a registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in $v registers for caller
  Return to place of call
§2.8 Supporting Procedures in Computer Hardware
jal MyPRoc
addi $sp, $sp, -n
jr $ra
96

## Slide 45: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)
97

## Slide 46: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction (PC) put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements
95

## Slide 47: Important Vocabulary
Caller: code executing the jal
Callee: destination of jal and calling jr $ra
Program Counter: $pc
Stack: memory located below stack pointer
Stack pointer: $sp
Push: decrement $sp, store word there
Pop: load word from $sp, increment $sp
98

## Slide 48: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in $a0, …, $a3
  f in $s0 (hence, need to save $s0 on stack)
  Result in $v0
A procedure that doesn’t call another procedure
98

## Slide 49: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Save return value
Restore $s0
Return
99

## Slide 50: Non-Leaf Procedures
Procedures that may call other procedures
For nested call, caller needs to save on the stack:
  Its return address (will be changed by jal)
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 51: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 52: Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
101

## Slide 53: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage
103
Before call
During call
After call

## Slide 54: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage
104

## Slide 55: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People
110

## Slide 56: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0
108

## Slide 57: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword
110

## Slide 58: String Copy MIPS Code
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return
108

## Slide 59: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers
141

## Slide 60: Example: Clearing an Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2
142

## Slide 61: Comparison of Array vs. Ptr
Multiply “strength reduced” to shift
Array version requires shift to be inside loop
  Part of index calculation for incremented i
  c.f. incrementing pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer
144

## Slide 62: Java and C
Very different languages and philosophies
Java is object-oriented and interpreted
C is a lower-level language, 30 years older than Java, and extremely fast
There is a great demand for both in the current marketplace
Java tends to be web front-end oriented
C is back-end

## Slide 63: ARM & MIPS Similarities
ARM: the most popular embedded core
Similar basic set of instructions to MIPS
§2.16 Real Stuff: ARM Instructions
 | ARM | MIPS
Date announced | 1985 | 1985
Instruction size | 32 bits | 32 bits
Address space | 32-bit flat | 32-bit flat
Data alignment | Aligned | Aligned
Data addressing modes | 9 | 3
Registers | 15 × 32-bit | 31 × 32-bit
Input/output | Memory mapped | Memory mapped
145

## Slide 64: ARM/MIPS instructions
146

## Slide 65: ARM/MIPS Addressing
147

## Slide 66: Compare and Branch in ARM
Uses condition codes for result of an arithmetic/logical instruction
  Negative, zero, carry, overflow
  Compare instructions to set condition codes without keeping the result
Each instruction can be conditional
  Top 4 bits of instruction word: condition value
  Can avoid branches over single instructions
147

## Slide 67: Instruction Encoding
148

## Slide 68: ARM Immediate Field
8 bits rotated right in a 32-bit register
2 times these four
0x102 becomes 0x8000000
148

## Slide 69: ARM LDM and STM
LDM = Load Multiple from stack
STM = Store Multiple to stack
16-bit mask indicates which registers
Options allow address pre- or post- increment or decrement
  And register to contain beginning or ending address
149

## Slide 70: The Intel x86 ISA
Evolution with backward compatibility
  8080 (1974): 8-bit microprocessor
    Accumulator, plus 3 index-register pairs
  8086 (1978): 16-bit extension to 8080
    Complex instruction set (CISC)
  8087 (1980): floating-point coprocessor
    Adds FP instructions and register stack
  80286 (1982): 24-bit addresses, MMU
    Segmented memory mapping and protection
  80386 (1985): 32-bit extension (now IA-32)
    Additional addressing modes and operations
    Paged memory mapping as well as segments
§2.17 Real Stuff: x86 Instructions
149

## Slide 71: The Intel x86 ISA
Further evolution…
  i486 (1989): pipelined, on-chip caches and FPU
    Compatible competitors: AMD, Cyrix, …
  Pentium (1993): superscalar, 64-bit datapath
    Later versions added MMX (Multi-Media eXtension) instructions
    The infamous FDIV bug
  Pentium Pro (1995), Pentium II (1997)
    New microarchitecture (see Colwell, The Pentium Chronicles)
  Pentium III (1999)
    Added SSE (Streaming SIMD Extensions) and associated registers
  Pentium 4 (2001)
    New microarchitecture
    Added SSE2 instructions
150

## Slide 72: The Intel x86 ISA
And further…
  AMD64 (2003): extended architecture to 64 bits
  EM64T – Extended Memory 64 Technology (2004)
    AMD64 adopted by Intel (with refinements)
    Added SSE3 instructions
  Intel Core (2006)
    Added SSE4 instructions, virtual machine support
  AMD64 (announced 2007): SSE5 instructions
    Intel declined to follow, instead…
  Advanced Vector Extension (announced 2008)
    Longer SSE registers, more instructions
If Intel didn’t extend with compatibility, its competitors would!
  Technical elegance ≠ market success
151

## Slide 73: Basic x86 Registers
153

## Slide 74: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement
153

## Slide 75: Example x86 Instructions
155
Instruction | Function
je name | If equal (condition code) {EIP=name}; EIP-128<=name<EIP+128
jmp name | EIP = name
call name | SP=SP-4; M[SP]=EIP+5; EIP=name;
movw EBX, [EDI+45] | EBX=M[EDI+45]
push esi | SP=SP-4; M[SP]=ESI;
pop edi | EDI=M[SP]; SP=SP+4;
add EAX, #C6765 | EAX=EAX+6765;
yest EDX, #42 | Set condition code (flags) with EDS and 42
movsl | M[EDI]=M[ESI]; EDI=EDI+4; ESI=ESI+4;
Want to learn how to do this?

## Slide 76: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …
157

## Slide 77: Implementing IA-32
Complex instruction set makes implementation difficult
  Hardware translates instructions to simpler microoperations
    Simple instructions: 1–1
    Complex instructions: 1–many
  Microengine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid complex instructions
157

## Slide 78: Conclusion about Intel
Intel had a 16-bit microprocessor two years before its competitors' more elegant architectures, such as the Motorola 68000, and this head start led to the selection of the 8086 as the CPU for the IBM PC. Intel engineers generally acknowledge that the x86 is more difficult to build than processors like ARMv7 and MIPS, but the large market meant in the PC Era that AMD and Intel could afford more resources to help overcome the added complexity. What the x86 lacks in style, it made up for in market size.
157

## Slide 79: ARM v8
64-bit version of the v7
Re-engineered from the bottom up
Conditional execution field eliminated
32 general registers
DIV instruction
Includes a zero register
BNE and BEQ instructions added
158

## Slide 80: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.18 Fallacies and Pitfalls
159

## Slide 81: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accumulate more instructions
x86 instruction set
161