## Slide 1: CS2160 Arithmetic for Computers

## Slide 2: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction
178

## Slide 3: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0
179

## Slide 4: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two + or two negative operands, no overflow
  Subtracting + from negative operand
    Overflow if result sign is 0
  Subtracting negative from positive operand
    Overflow if result sign is 1
179

## Slide 5: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action
180

## Slide 6: Overflow Indicators
180

## Slide 7: Handling Overflow
Causes an interrupt or an exception to occur
  There are HW and SW interrupts
    MIPS uses a software interrupt for overflow
    So it has to actually check for it
  OS is called to take care of the situation
    Finds out what caused the problem
    Decides if something needs to be fixed or ignored
    Does the fix if appropriate
    Ignores if appropriate
    Terminates program if necessary.
180

## Slide 8: Interrupt Handling in General
MIPS processor stores PC after exception in EPC register (exception program counter)
  Remember, this is the instruction _after_ the one that caused the exception
  Handler has to decide if it needs to return to the instruction that caused the problem, just continue, or abort.
Registers $k0 and $k1 reserved for OS (kernel) use.
182

## Slide 9: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
Shift left each subsequent bit and add to product if bit was 1
Elementary school approach
183

## Slide 10: Multiplication Hardware
Initially 0
1000
1001
00000000
00001000
01001000
0100
0010
0001
10000
100000
1000000
184

## Slide 11: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low
1001
00000000
1000
00001000
000001000
0000001000
00000001000
00001001000
0100
0010
0001
186

## Slide 12: Signed Multiplication
Remember original signs
Convert numbers to unsigned
Multiply
Change sign of result if indicated by signs of operands.
  S = S1 XOR S2
187

## Slide 13: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplications performed in parallel
188
5 levels

## Slide 14: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd
    Hi bits are lost
No destination
188

## Slide 15: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division
189

## Slide 16: Division Hardware
Initially dividend
Initially divisor in left half
190

## Slide 17: Division Example
7 / 2 = 3 r 1
0000
0000 0111
0010 0000
0001
0011
0001 0000
0000 1000
0000 0100
0000 0010
0000 0001
1110 0111
1111 0111
1111 1111
0000 0011
0000 0001
+
-
190

## Slide 18: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both
192

## Slide 19: Hardware Comparison
They look about the same

## Slide 20: Signed Division
Like multiplication, the sign of the quotient is an XOR of the signs of the operands
The sign of the remainder is more difficult
Rule must always hold:
  Dividend = Quotient * Divisor + Remainder
  Remainder = Dividend – Quotient * Divisor
7 / -2 : -3 remainder 1
-7 / -2: 3 remainder -1
193

## Slide 21: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps
  Use lookup tables
Sweeney, Robertson, and Tocher
194

## Slide 22: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi(r), mflo(q) to access result
194

## Slide 23: Binary Fixed Point
Decimal fractions can be represented in binary
  Sometimes not easily
  Same rules apply as for decimal
  Positive powers to the left of the point, negative powers to the right
So 1.5 in decimal is 1.1 in binary
1.125 in decimal is 1.001 in binary
5.625 is decimal is 101.101 in binary
0.1 in decimal is 0.000110011001100110011…

## Slide 24: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double
normalized
not normalized
§3.5 Floating Point
197

## Slide 25: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two common representations
  Single precision (32-bit)
  Double precision (64-bit)
  Half-precision and quad-precision also available
198

## Slide 26: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
198

## Slide 27: Representations
199

## Slide 28: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38
198

## Slide 29: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308
298

## Slide 30: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision
201

## Slide 31: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00
201

## Slide 32: Floating-Point Example
What number is represented by the single-precision float 0xC0A00000
11000000101000…00
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0
202

## Slide 33: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 34: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 35: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102
203

## Slide 36: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625
203

## Slide 37: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 38: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 39: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106
206

## Slide 40: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875
206

## Slide 41: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined
211

## Slide 42: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
    e.g., ldc1 $f8, 32($sp)
211

## Slide 43: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le, …)
  Sets or clears FP condition-code bit
    e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  bc1t, bc1f
    e.g., bc1t TargetLabel
211

## Slide 44: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals in global memory space
Compiled MIPS code:
f2c: lwc1 $f16, const5($gp) lwc2 $f18, const9($gp) div.s $f16, $f16, $f18 lwc1 $f18, const32($gp) sub.s $f18, $f12, $f18 mul.s $f0, $f16, $f18 jr $ra
214

## Slide 45: FP Example: Array Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[][], double y[][], double z[][]) { int i, j, k; for (i = 0; i< 32; i++) for (j = 0; j < 32; j++) for (k = 0; k < 32; k++) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in $a0, $a1, $a2, and i, j, k in $s0, $s1, $s2
215

## Slide 46: Illustrated
X
X
Y
Z
=
+
x

## Slide 47: FP Example: Array Multiplication
MIPS code:
li $t1, 32 # $t1 = 32 (row size/loop end) li $s0, 0 # i = 0; initialize 1st for loop L1: li $s1, 0 # j = 0; restart 2nd for loop L2: li $s2, 0 # k = 0; restart 3rd for loop sll $t2, $s0, 5 # $t2 = i * 32 (size of row of x) addu $t2, $t2, $s1 # $t2 = i * size(row) + j sll $t2, $t2, 3 # $t2 = byte offset of [i][j] addu $t2, $a0, $t2 # $t2 = byte address of x[i][j] l.d $f4, 0($t2) # $f4 = 8 bytes of x[i][j] L3: sll $t0, $s2, 5 # $t0 = k * 32 (size of row of z) addu $t0, $t0, $s1 # $t0 = k * size(row) + j sll $t0, $t0, 3 # $t0 = byte offset of [k][j] addu $t0, $a2, $t0 # $t0 = byte address of z[k][j] l.d $f16, 0($t0) # $f16 = 8 bytes of z[k][j] …
216

## Slide 48: FP Example: Array Multiplication
… sll $t0, $s0, 5 # $t0 = i*32 (size of row of y) addu $t0, $t0, $s2 # $t0 = i*size(row) + k sll $t0, $t0, 3 # $t0 = byte offset of [i][k] addu $t0, $a1, $t0 # $t0 = byte address of y[i][k] l.d $f18, 0($t0) # $f18 = 8 bytes of y[i][k] mul.d $f16, $f18, $f16 # $f16 = y[i][k] * z[k][j] add.d $f4, $f4, $f16 # f4=x[i][j] + y[i][k]*z[k][j] addiu $s2, $s2, 1 # $k k + 1 bne $s2, $t1, L3 # if (k != 32) go to L3 s.d $f4, 0($t2) # x[i][j] = $f4 addiu $s1, $s1, 1 # $j = j + 1 bne $s1, $t1, L2 # if (j != 32) go to L2 addiu $s0, $s0, 1 # $i = i + 1 bne $s0, $t1, L1 # if (i != 32) go to L1
217

## Slide 49: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
§3.6 Parallelism and Computer Arithmetic: Associativity
Need to validate parallel programs under varying degrees of parallelism

## Slide 50: Interpretation of Data
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
The BIG Picture

## Slide 51: Floating Point Conversion
Decimal to Binary
  Convert -13.375 to single-precision binary floating point (express in hex)
  Sign bit is 1
  Number in binary is 1101.011
  Number in scientific notation is 1.101011 x 23
  Fraction (omitting initial 1) is 101011
  Exponent is 3 + 127 = 130 = 10000010
  S-E-F is 1- 10000010-101011 000…
  Group by 4’s
  1100 0001 0101 0110 00…
  0xC1560000

## Slide 52: Floating Point Conversion
Hexadecimal IEEE-754 to decimal
Example: 0x40480000
Write in binary: 0100 0000 0100 1000 0000…
Group into S-E-F: 0 10000000 10010000000…
S = 0 (number is positive)
E is 128, so power of 2 is 128-127 = 1
Reconstitute F: 1.1001
Write in scientific notation: 1.1001 x 21
11.001
= 3.125

## Slide 53: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles

## Slide 55: Chronology
July 1994: Intel discovers the bug in the Pentium. The actual cost to fix the bug was several hundred thousand dollars.
September 1994: A math professor at Lynchburg College in Virginia, Thomas Nicely, discovers the bug, After calling Intel technical support and getting no official reaction, he posts his discovery on the Internet.

## Slide 56: Chronology 2
November 22, 1994: Intel issues a press release, calling it a "glitch." The Pentium "can make errors in the ninth digit. ... Even most engineers and financial analysts require accuracy only to the fourth or fifth decimal point.
December 5,1994: Intel claims the flaw happens once in 27,000 years
December 12,1994: IBM Research Division days once every 24 days

## Slide 57: Chronology 3
December 21, 1994: Intel releases the following, signed by Intel's president:
Analysts estimate that this recall cost Intel $500 million, and Intel engineers did not get a Christmas bonus that year.

## Slide 58: Subword Parallelism
Remember parallelism means there’s a pattern to something
  In this case, it’s the same operation done on different data
Subword refers to divisions in data smaller than a word (or register)
Involves use of carry partitions in registers
  Blocks the cascading of a carry to the next digit to the left.
Adds use the same circuitry, but can be done in parallel
  128-bit register can handle 2 64-bit words, 4 32-bit values, 8 16-bit values, etc.
222

## Slide 59: Subword Parallelism is also
Data-level parallelism
Single instruction multiple data (Flynn’s taxonomy)
222

## Slide 60: The ARM implementation
Called NEON
About 100 instructions
223

## Slide 61: The Intel Implementation
Multimedia extensions (MMX)
Streaming SIMD extension (SSE and SSE2)
Added 144 instructions
Eight 64-bit fp registers
AMD doubled the registers and called it XMM
Intel did the same thing and called it EM64T
Intel added 128-bit registers
Can operate on 4 single-precision or 2 double-precision numbers

## Slide 62: Advanced Vector Extensions (AVX)
Intel, 2011
256-bit registers
Arithmetic instructions can now be three registers (instead of two)
Need new load/store instructions
  Can read aligned or unaligned

## Slide 63: DGEMM
Double Precision, General Matrix Multiply.`
void dgemm (int n, double* A, double* B, double* C)
{
for (int i 0; i < n; ++i )
for (int j = 0; j < n; ++j)
{
double cij C[i+j*n];
for( int k = 0; k < n; k++ )
cij += A[i+k*n] * B[k+j*n];
C[i+j*n] = cij;
}
}
Unoptimized code

## Slide 64: Doing four things at a Time
=
x

## Slide 65: Optimized code
#include <x86intrin.h>
void dgemm (int n. double* A, double* B, double* C)
{
for ( int i 0 ; i < n ; i +=4 )
for ( int j = 0; j < n; j++ )
{
_m256d cO = _mm256_load_pd(C+i+j*n);
for( int k = 0; k < n; k++ )
cO = _mm 256_add_pd (c0,
_mm 256_mul _pd (_mm 256_l oad_pd(A+i+k*n),
_mm 256_broadcast_sd(B+k+j*n )));
_mm 256_store_pd(C+i+j*n . cO);
}
}

## Slide 66: Comments about shortcuts
Shifting left and right are shortcuts for multiply and divide
  Unsigned only
  No overflow
Associativity of floating point ops in parallel

## Slide 67: MIPS Core Instructions
Those executed on the hardware
Not pseudo instructions
Whole set of real and pseudo instructions called MIPS 32
Core instructions cover most needs

## Slide 68: Floating Point Exercises
-12.5 0xc1480000
15.875 0x417e0000
33.75 0x42070000
-0.0625 0xbd800000