## Slide 1: CS 2160 Parallel Processors
Chapter 6

## Slide 2: Introduction
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability, availability, power efficiency
Job-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)
§9.1 Introduction
502

## Slide 3: Hardware and Software
Hardware
  Serial: e.g., Pentium 4
  Parallel: e.g., quad-core Xeon e5345
Software
  Sequential: e.g., matrix multiplication
  Concurrent: e.g., operating system
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware
503

## Slide 4: What We’ve Already Covered
§2.11: Parallelism and Instructions
  Synchronization
§3.6: Parallelism and Computer Arithmetic
  Associativity
§4.10: Parallelism and Advanced Instruction-Level Parallelism
§5.8: Parallelism and Memory Hierarchies
  Cache Coherence
§6.9: Parallelism and I/O:
  Redundant Arrays of Inexpensive Disks
504

## Slide 5: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§7.2 The Difficulty of Creating Parallel Processing Programs
504

## Slide 6: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90× speedup?
  Tnew = Tparallelizable/100 + Tsequential
  90-90F+.9F = 1
  89 = 90F-.9F
  F = 89/89.9
  ~ 0.999
Need sequential part to be 0.1% of original time
505

## Slide 7: Strong vs Weak Scaling
Strong scaling: problem size fixed
Weak scaling: problem size proportional to number of processors
  I.e., parallelizing the solution adds processing overhead
507

## Slide 8: Flynn’s Taxonomy
509
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345
SPMD: Single Program Multiple Data
  A parallel program on a MIMD computer
  Conditional code for different processors

## Slide 9: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§7.3 Shared Memory Multiprocessors
510

## Slide 10: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications
511

## Slide 11: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to MIPS
  32 × 64-element registers (64-bit elements)
  Vector instructions
    lv, sv: load/store vector
    addv.d: add vectors of double
    addvs.d: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth
511

## Slide 12: Example: DAXPY (Y = a × X + Y)
Conventional MIPS code
l.d $f0,a($sp) ;load scalar a addiu r4,$s0,#512 ;upper bound of what to load loop: l.d $f2,0($s0) ;load x(i) mul.d $f2,$f2,$f0 ;a × x(i) l.d $f4,0($s1) ;load y(i) add.d $f4,$f4,$f2 ;a × x(i) + y(i) s.d $f4,0($s1) ;store into y(i) addiu $s0,$s0,#8 ;increment index to x addiu $s1,$s1,#8 ;increment index to y subu $t0,r4,$s0 ;compute bound bne $t0,$zero,loop ;check if done
Vector MIPS code
l.d $f0,a($sp) ;load scalar a lv $v1,0($s0) ;load vector x mulvs.d $v2,$v1,$f0 ;vector-scalar multiply lv $v3,0($s1) ;load vector y addv.d $v4,$v2,$v3 ;add y to product sv $v4,0($s1) ;store the result
511

## Slide 13: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology
512

## Slide 14: Vector Memory Access
Strided
  Constant distance between elements
Indexed
  Vector contains addresses which should be loaded
    Variable distance between elements

## Slide 15: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
  Allows for multiple hardware lanes
Vector Architectures
514

## Slide 16: Hardware Multithreading
Hardware Multithreading
  Increasing utilization of a processor by switching to another thread when one thread is stalled.
Thread
  A thread includes the program counter, the register state, and the stack. It is a lightweight process; whereas threads commonly share a single address space, processes don't.
Process
  one or more threads, the address space, and the operating system state. Hence, a process switch usually invokes the operating system, but not a thread switch.
Fine-Grained Multithreading
  Switching between threads after every instruction.
Coarse-Grained Multithreading
  Switching between threads only after significant events, such as a last-level cache miss.
516

## Slide 17: Multithreading Example
517

## Slide 18: Multithreading Speedup
518

## Slide 19: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§7.4 Clusters and Other Message-Passing Multiprocessors
520
NUMA
UMA

## Slide 20: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
  Initial summation on each processor
  sum[Pn] = 0; for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1) sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums
  Reduction: divide and conquer
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps
521

## Slide 21: Example: Sum Reduction
half = 100;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* Conditional sum needed when half is odd;
Processor0 gets missing element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);
521

## Slide 22: Sum Reduction (Again)
Given send() and receive() operations
  limit = 100; half = 100;/* 100 processors */ repeat half = (half+1)/2; /* send vs. receive dividing line */ if (Pn >= half && Pn < limit) send(Pn - half, sum); if (Pn < (limit/2)) sum = sum + receive(); limit = half; /* upper limit of senders */ until (half == 1); /* exit with final sum */
  Send/receive also provide synchronization
  Assumes send/receive take similar time to addition

## Slide 23: Synchronization Summary
Is necessary
Slows down the process, but makes it correct
Method (synch barrier or comms bus) makes little difference

## Slide 24: Introduction to GPUs
How are GPUs different from CPUs?
  GPUs supplement a CPU; there are still serial tasks to be done
  GPU problem sizes are typically hundreds of megabytes to gigabytes, but not hundreds of gigabytes to terabytes
  Do not rely on multilevel caches to overcome the long latency to memory
  Memory is oriented toward bandwidth rather than latency.
  Each GPU processor is more highly multithreaded than a typical CPU, plus they have more processors.
525

## Slide 25: Introduction to NVIDIA GPUs
526

## Slide 26: NVIDIA Fermi Specs
One SIMD instruction, 32 threads, 16 lanes
  2 clocks per instruction
Fine-grained multithreading
  Thread schedule can schedule any thread in any lane
32K 32-bit registers
  2K threads per lane
  <= 64 registers per thread
527

## Slide 27: Memory Allocation
528

## Slide 28: SIMD CPUs vs SIMD GPUs
529

## Slide 29: CPU vs GPU Terminology
530

## Slide 30: Clusters, Warehouse-Scale Machines
Machines in a cluster, if working on the same problem must communicate
Communication is non-uniform
  Takes longer to communicate with some processors than others
OSs have send routines and receive routines
  Synchronous or blocking
  Asynchronous or non-blocking
531

## Slide 31: Warehouse Scale computing
Used by Google, Amazon, etc
100,000 servers in a warehouse
Huge quantitative difference in size results in qualitative differences
  Energy efficiency important
  Reliability important
532

## Slide 32: Map-Reduce
Method of using massively parallel architectures to solve impossible serial problems
Map: Parallel creation of independent, intermediate results
Reduce: Aggregation of intermediate results into final product
533

## Slide 33: Major WSC-Datacenter Differences
WSCs provide one set of applications for a million users, data centers provide a suite of apps for hundreds or maybe thousands of users
WSCs need ample, easy parallelism to be efficient
Operational costs of WSCs are more significant
WSCs have larger economies of scale

## Slide 34: Grid Computing
E.g., SETI@home
Started by UC Berkeley in 1999
Leverages ~5 million idle PCs around the world
Centrally coordinated problem solving
3.5 Petaflops and the end of 2011
535

## Slide 35: Interconnection Networks
Network topologies
  Arrangements of processors, switches, and links
§6.8 Introduction to Multiprocessor Network Topologies
Bus
Ring
2D Mesh
N-cube (N = 3)
Fully connected
536

## Slide 36: Some Definitions
Network Bandwidth: the peak transfer rate of a network; often the sum of bandwidth of all the links in the network.
Bisection Bandwidth: The bandwidth between two equal parts of a multiprocessor. This measure is for a worst-case split of the multiprocessor.
Multistage Network: a switch at each node
Crossbar Network: any node can communicate with any other node in one pass through the network
537

## Slide 37: Multistage Networks
539

## Slide 38: Network Characteristics
Performance
  Latency per message (unloaded network)
  Throughput
    Link bandwidth
    Total network bandwidth
    Bisection bandwidth
  Congestion delays (depending on traffic)
Cost
Power
Routability in silicon

## Slide 39: Code or Applications?
Traditional benchmarks
  Fixed code and data sets
  Sensitive only to improvements in architecture and compilers
Parallel programming is evolving
  Should algorithms, programming languages, and tools be part of the system?
  Compare systems, provided they implement a given application
  E.g., Linpack, Berkeley Design Patterns
Would foster innovation in approaches to parallelism
540

## Slide 40: Parallel Benchmarks
Linpack: matrix linear algebra
SPECrate: parallel run of SPEC CPU programs
  Job-level parallelism
SPLASH: Stanford Parallel Applications for Shared Memory
  Mix of kernels and applications, strong scaling
NAS (NASA Advanced Supercomputing) suite
  computational fluid dynamics kernels
PARSEC (Princeton Application Repository for Shared Memory Computers) suite
  Multithreaded applications using Pthreads and OpenMP
§6.10 Multiprocessor Benchmarks and Performance Models
540

## Slide 41: Modeling Performance
Assume performance metric of interest is achievable GFLOPs/sec
  Measured using computational kernels from Berkeley Design Patterns
Arithmetic intensity of a kernel
  FLOPs per byte of memory accessed
For a given computer, determine
  Peak GFLOPS (from data sheet)
  Peak memory bytes/sec (using Stream benchmark)
542

## Slide 42: Arithmetic Intensity
543

## Slide 43: Roofline Diagram
Attainable GPLOPs/sec
= Max ( Peak Memory BW × Arithmetic Intensity, Peak FP Performance )
544

## Slide 44: Comparing Systems
Example: Opteron X2 vs. Opteron X4
  2-core vs. 4-core, 2× FP performance/core, 2.2GHz vs. 2.3GHz
  Same memory system
To get higher performance on X4 than X2
  Need high arithmetic intensity
  Or working set must fit in X4’s 2MB L-3 cache
546

## Slide 45: Optimizing Performance
Optimize FP performance
  Balance adds & multiplies
  Improve superscalar ILP and use of SIMD instructions
Optimize memory usage
  Software prefetch
    Avoid load stalls
  Memory affinity
    Avoid non-local data accesses
548

## Slide 46: Optimizing Performance
Choice of optimization depends on arithmetic intensity of code
Arithmetic intensity is not always fixed
  May scale with problem size
  Caching reduces memory accesses
    Increases arithmetic intensity
549

## Slide 47: i7-960 vs. NVIDIA Tesla 280/480
§6.11 Real Stuff: Benchmarking and Rooflines i7 vs. Tesla
551
Typo. Ha ha.

## Slide 48: Rooflines
552