## Slide 1: CS 2160 Chapter 1
Abstractions and Technology

## Slide 2
The Computer Revolution
Began in the 1940s
Now accounts for 10% of GNP
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Density doubles every 18-24 months
3

## Slide 3: Classes of Computers
Desktop computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints
  Update
    Personal mobile devices
    Warehouse computing systems
Single User
Multiple Users
Device-Dependent
5

## Slide 4: The Processor Market
7
"c:'
  O+---- -
2007 2008 2009 2010 2011 2012
Exponential Rise

## Slide 5: What You Will Learn
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
What is parallel processing
8

## Slide 6: Understanding Performance
Algorithm
  Determines number of operations executed
  Not so much covered in this book
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed
9

## Slide 7: 8 Great Architecture Ideas
Design for Moore’s Law
Use abstractions to simplify design
Make the common case fast
Parallelism
Pipelining
Prediction
Memory Hierarchy
Reliability via Redundancy
11

## Slide 8: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.2 Below Your Program
13

## Slide 9: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data
Translates high-level code into low-level instructions
Translates low-level instructions into machine(like) code
15

## Slide 10: That was Then, This is Now
Previous slide is the compile-assemble-link process that is used in languages like C or C++
Java and C# use a different process
  Source code compiled to byte code
    Byte code is machine independent
    Java Byte Code for Java, Microsoft Intermediate Language (MSIL) for C#
Executed by a machine-specific run-time
  Java Virtual Machine for Java, .Net Framework for Microsoft

## Slide 11: Writing Assembly Code
MIPS Assembler and Runtime Simulator
Download from Blackboard
It’s a .jar file, so double-clicking on the file will run it

## Slide 12: The strcpy Example
.data #data declarations follow
Source:
.asciiz "A string to copy. " # Source string
Dest:
.asciiz “ " #Blank space into which to copy the source string
.text # assembly code follows
la $a1, Source
la $a0, Dest
jal strcpy
li $v0, 10 #loads op code into $v0 to exit program
syscall #reads $v0 and exits program
strcpy:
addi $sp, $sp, -4 # adjust stack for 1 item
sw $s0, 0($sp) # save $s0
add $s0, $zero, $zero # i = 0
L1: add $t1, $s0, $a1 # addr of y[i] in $t1
lbu $t2, 0($t1) # $t2 = y[i]
add $t3, $s0, $a0 # addr of x[i] in $t3
sb $t2, 0($t3) # x[i] = y[i]
beq $t2, $zero, L2 # exit loop if y[i] == 0
addi $s0, $s0, 1 # i = i + 1
j L1 # next iteration of loop
L2: lw $s0, 0($sp) # restore saved $s0
addi $sp, $sp, 4 # pop 1 item from stack
jr $ra # and return

## Slide 13: Run MARS
Select File | New
Paste in strcpy code

## Slide 14: Save and Assemble
Save file
Select
Run | Assemble

## Slide 15: Step Through Program with f7

## Slide 16: For Next Time
Not graded, but…
  Download MARS from Blackboard
  Try pasting in the strcpy code and running it, step-by-step
  See if you understand what’s happening in the registers and in memory

## Slide 17: Components of a Computer
Same components for all kinds of computer
  Desktop, server, embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers
§1.3 Under the Covers
The BIG Picture
17

## Slide 18
Email: put CS 2160 in the subject line, or at least mention it in the e-mail.
  May not be able to give HW help within 24 hrs of the due time.
Homework

## Slide 19: Anatomy of a Mouse
Optical mouse
  LED illuminates desktop
  Small low-res camera
  Basic image processor
    Looks for x, y movement
  Buttons & wheel
Supersedes roller-ball mechanical mouse

## Slide 20: Anatomy of a Mouse
Optical mouse
  LED illuminates desktop
  Small low-res camera
  Basic image processor
    Looks for x, y movement
  Buttons & wheel
Supersedes roller-ball mechanical mouse

## Slide 21: Inside a Laptop
Major features are chips and connectors: things that do things and move things around

## Slide 22: Through the Looking Glass
This is old technology. Currently Liquid Crystal Displays are used with Active Matrix technology.
In color graphics, each picture element (pixel) on the screen represents at least 24 bits of data
18

## Slide 23: Touch Screens
Replacement for keyboard and mouse
  Great for mobile devices
Capacitive sensing
  Presence of a finger or conductive stylus can be sensed by a change in the electrostatic field on the screen
  Multiple-touch technology allows interpretation of multiple hot spots, usually used to expand and contract display sizes.
19

## Slide 24: Inside an iPad
Metal back
Bezel
Batteries
Screen
“Motherboard”
Wifi/FM/
Bluetooth
Camera, headphone
Jack, microphone
Display lock/
Accelerometer
Speaker
Cable
Touch screen controller
20

## Slide 25: Inside the Processor (CPU)
Datapath: performs operations on data (arithmetic)
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data
21

## Slide 26: Inside the Processor
2-core ARM 5
10 x 12 mm
Includes
  graphics processor
  Cache memory
  Wireless interface
  Audio interface
  Memory interface
  I/O interface
21

## Slide 27: Inside the Processor
AMD Barcelona: 4 processor cores

## Slide 28: Memory Hierarchy
L1 cache
L2 cache
L3 Cache
Main Memory
Local Disk (magnetic or solid-state)
Other storage
  Optical disks
  Network or remote storage
SRAM
DRAM
Volatile memory
Non-volatile memory
23

## Slide 29: More on Cache
Multiple levels
  Typically L1, L2 on chip, per core
  L3 on or off chip, shared
  Main memory and Disk system are extensions
  On-chip memory typically Static Random Access Memory (SRAM)
    Uses more power, produces more heat, is faster
  Main memory Dynamic RAM
    Requires refresh cycles
    Slower
    Way cheaper

## Slide 30: Networks
Communication and resource sharing
Local area network (LAN): Ethernet
  Within a building
Wide area network (WAN: the Internet
Wireless network: WiFi, Bluetooth
Long Range
(100 m)
Short Range
(1 m)

## Slide 31: Network Balance Sheet
Advantages
Disadvantages
Resource sharing
Remote access
Convenience
Distributed nature
Security
Speed
Node failure

## Slide 32: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2005 | Ultra large scale IC | 6,200,000,000 | 
DRAM capacity
Moore’s Law

## Slide 33: What’s a Transistor?
Old style
(Discreet components)
Base
Collector
Emitter
It’s a switch that uses the base to control the current flowing between the collector and emitter.
It comes in two varieties: PNP (shown) and NPN based on the positive or negative doping of the silicon layers
Replaced vacuum tubes
More recently:

## Slide 34: Chip Fabrication Process
26

## Slide 35: Wafer with Dies
Wasted space, but not worth masking
Intel Core i7
12” wafer
100% yield = 280
32nm process
20.7 x 10.5mm die
27

## Slide 36: Binary Refresher
210 is roughly 1000 (1024, actually)
So 210 is about 103
Thus:
Binary | Decimal | Decimal Name
210 | 103 | Kilo-
220 | 106 | Mega-
230 | 109 | Giga-
240 | 1012 | Tera-
250 | 1015 | Peta-

## Slide 37: More About Binary
Can be used to represent
  Integers
    ±231 or ±about 2 billion
  Floating point numbers
    32-bit (single precision) or 64-bit
    Bits of exponent determine range (8 bits--2256)
    Bits of fraction determine precision
  Characters
    8-bit, 16-bit, multi-byte
  Images
    TIFF, GIF, JPG, PNG, etc.

## Slide 38: Bases of Numbers
Decimal – base 10
Octal – base 8
Binary – base 2
Hexadecimal – base 16
The only hard one is…decimal

## Slide 39: Base 2 (binary)
20
21
22
23
24
25
26
27
128
64
32
16
8
4
2
1
1
0
1
1
0
1
0
1
= 128 + 32 + 16 + 4 + 1
= 181

## Slide 40: Conversion Among non-Decimal Bases
1101011011110001101101010110001000010011110110100100010
Binary
1101011011110001101101010110001000010011110110100100010
Octal
1 5 3 3 6 1 5 5 2 6 2 0 2 3 6 6 4 4 2
1101011011110001101101010110001000010011110110100100010
Hexadecimal
6 B 7 8 C A B 1 0 9 E C 2 2

## Slide 41: Binary Floating Point
Start with decimal floating point: 101.125
102
101
100
10-1
10-2
10-3
Binary works the same way: 1100101.001
2-2
2-1
2-3
22
21
20

## Slide 42: Defining Performance
Which airplane has the best performance?
§1.4 Performance
29

## Slide 43: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…
30

## Slide 44: Relative Performance
Define Performance = 1/Execution Time
“X is n times faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B
Performance and execution time are inversely related
30

## Slide 45: Talking About Performance
Machine A is faster than machine B if
  The same work takes less time on machine A
  Machine A does more than machine B in the same (or less) time
If A is x times faster than B (and A is, in fact, faster) then x > 1
The percentage by which A is faster than B is given by (x - 1)*100
  i.e., 1.25 -> faster by 25%; 2.5 -> faster by 150%

## Slide 46: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 47: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 48: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 49: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?
34

## Slide 50: Bandwidth and Latency
Log-log plot of bandwidth and latency milestones
Trends in Technology

## Slide 51: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much
35

## Slide 52: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix
37

## Slide 53: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency
37

## Slide 54: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5
37

## Slide 55: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture
Time is the most complete measure of performance
38

## Slide 56: Come and See My Etchings…
Complementary Metal Oxide Semiconductor
  Used in almost all CPU and memory manufacturing today
  Combination of positive doped and negative doped areas on the silicon
  Manufacture involves successive steps of depositing/growing metal layers and etching them
  P-type and N-type transistors are interleaved to facilitate connection and lower power drain

## Slide 57: Power Trends
In CMOS IC technology
§1.5 The Power Wall
×1000
×30
5V → 1V
40

## Slide 58: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?
41

## Slide 59: Uniprocessor Performance
§1.6 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency
44

## Slide 60: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 61: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to a reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)
48

## Slide 62: In the Current News
“Exponential growth depends on three levels of adoption in the computing ecosystem. The chip level is the domain of Moore's Law, as noted. However, the faster chips cannot realize their potential unless the host computer system supports the faster speeds and unless application workloads provide sufficient parallel computational work to keep the chips busy. And the faster systems cannot reach their potential without rapid adoption by the user community. The improvement process at all three levels must be exponential; otherwise, the system or community level would be a bottleneck, and we would not observe the effects often described as Moore's Law.”
(Communications of the ACM, January 2017, pp 54-65.)

## Slide 63: Intel pursues Moore's Law with plan to make 7-nm chips this year
Intel's next big Moore's Law advance will be a 7-nm pilot plant it is establishing this year to explore the upcoming manufacturing process. The chipmaker announced it was establishing the pilot plant during an earnings call on Thursday, January 26.

## Slide 64: Amdahl’s Law
1922-2015
Exec time = time affected by improvement + time not affected by improvement
Assume parallelizable part is reduced proportional to the number of processors
Serial Process
Parallelizable Process
1
3
49

## Slide 65
Serial Process
Parallelizable Process
1
3
With 3 processors:
Serial Process
Parallel Process
1
3/3 = 1
Process now takes 2 units to complete instead of 4
What if we had infinite processors?
49

## Slide 66: General Formula
Speedup Factor =
1
Serial fraction +
Parallel fraction
Number of processors
=
1
0.25 + 0.75 / 3
=
1/0.5 = 2
49

## Slide 67: Interesting Stuff
36-core, 1.2GHz chip
New IBM Machine
Longer Battery Life