## Slide 1: CS 2160 Memory Hierarchy
Chapter 5

## Slide 2: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB (2014 $1000/GB)
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB (2014 $8/GB)
USB Flash
  30ns – 60 ns, (2014 $0.94/GB)
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB (2014 $0.04/GB)
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
§5.1 Introduction
375

## Slide 3: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
375

## Slide 4: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU
375

## Slide 5: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level
375

## Slide 6: Static RAM Technology
Typically 6 transistors per bit
State stored as a stable state among transistors
Other designs trade power for number of transistors.
379

## Slide 7: Dynamic RAM Technology
Charge stored as capacitance, not a transistor state
  Fewer transistors (1-2), less current than SRAM
Charge only lasts a few milliseconds
  Refresh cycle reads and rewrites each bit
Synchronous DRAM can transfer long blocks of bits without intermittently specifying an address
379

## Slide 8: Double Data Rate DRAM
A type of SDRAM
Transfers data on rising and falling edge of clock cycle
DDR3: 400 - 1066 MHz, therefore up to 2133 M transfers/sec (64 bits wide)
Main memory typically provided with 4-16 DRAM chips on a DIMM board
4-8 byte bus width
380

## Slide 9: Flash Memory
Based on EEPROM technology (Electrically Erasable Programmable Read Only Memory)
State stored as the polarity of a charged substance
Has a limited number of writes
Wear leveling used to distribute writes among blocks of memory
Can also be done by OS
SSD drives have DRAM buffers
381

## Slide 10: Disk Memory
Disk composed of platters
Top and bottom of platter hold data
Access time composed of seek time and rotational latency
382

## Slide 11: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.2 The Basics of Caches
How do we know if the data is present?
Where do we look?
385

## Slide 12: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits
385

## Slide 13: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 14: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 15: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Dec word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
386

## Slide 16: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 17: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 18: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 19: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 20: Address Subdivision
389

## Slide 21: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 22: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 23: Miss Rate vs Block Size
391

## Slide 24: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access
392

## Slide 25: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full
393

## Slide 26: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first
394

## Slide 27: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 28: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%
395

## Slide 29: Example: Intrinsity FastMATH
396

## Slide 30: Main Memory Supporting Caches
Use DRAMs for main memory
  Fixed width (e.g., 1 word)
  Connected by fixed-width clocked bus
    Bus clock is typically slower than CPU clock
Example cache block read
  1 bus cycle for address transfer
  15 bus cycles per DRAM access
  1 bus cycle per data transfer
For 4-word block, 1-word-wide DRAM
  Miss penalty = 1 + 4×15 + 4×1 = 65 bus cycles
  Bandwidth = 16 bytes / 65 cycles = 0.25 B/cycle

## Slide 31: Increasing Memory Bandwidth
4-word wide memory
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  Bandwidth = 16 bytes / 17 cycles = 0.94 B/cycle
4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 B/cycle

## Slide 32: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
Quad data rate (QDR) DRAM
  Separate DDR inputs and outputs

## Slide 33: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50

## Slide 34: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:
§5.3 Measuring and Improving Cache Performance

## Slide 35: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster
401

## Slide 36: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction
402

## Slide 37: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 38: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)
403

## Slide 39: Associative Cache Example
403

## Slide 40: Spectrum of Associativity
For a cache with 8 entries
404

## Slide 41: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
405

## Slide 42: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 
406

## Slide 43: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%
407

## Slide 44: Set Associative Cache Organization
406

## Slide 45: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity
409

## Slide 46: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache
410

## Slide 47: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9
410

## Slide 48: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6
410

## Slide 49: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 50: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 51: Interactions with Software
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access
412

## Slide 52: DGEMM Matrix Multiply Optimizations
x
=
Basic concept:
But cache use is very unoptimized
Instead, break problem into sub-problems
414

## Slide 53: Optimization Comparisons
416

## Slide 54: Dependable Memory Hierarchy
Service accomplishment, where the service is delivered as specified
Service interruption, where the delivered service is different from the specified service
Thus, require service-level agreement
418

## Slide 55: Availability
Mean Time to Fail (MTTF)
Mean Time to Repair (MTTR)
Mean Time Between Failures (MTBF)
  MTTF + MTTR
Availability: MTTF/MTBF
419

## Slide 56: Hamming ECC
Memory is no good if it isn’t reliable
Bit failures increase with time
Can use parity to detect errors
But parity alone can’t correct errors
  Except for one bit
Can use an interplay of parities to correct single failures in more bits
420

## Slide 57: How Hamming ECC Works
Start numbering bits from 1 on the left, as opposed to the traditional numbering of the rightmost bit being 0.
Mark all bit positions that are powers of 2 as parit
All other bit positions are used for data bits (positions 3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15, . .. ).y bits (positions 1, 2, 4, 8, 16, ... ) .
Parity bit 2n check is parity for bits whose position number has bit n = 1.
420

## Slide 58: Hamming ECC
Bit position | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | p1 | p2 | d1 | p4 | d2 | d3 | d4 | p8 | d5 | d6 | d7 | d8
 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1
P1 is even parity for d1, d2, d4, d5, and d7 (0, 1, 0, 0, 0) = 1
P2 is even parity for d1, d3, d4, d6, d7 (0, 0, 0, 0, 0) = 0
P4 is even parity for d2, d3, d4 and d8 (1, 0, 0, 1) = 0
P8 is even parity for d5, d6, d7, d8 (0, 0, 0, 1) = 1
421
Bit 0 =1
Bit 1 = 1
Bit 2 = 1
Bit 3 = 1

## Slide 59: How it works
Bit position | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | p1 | p2 | d1 | p4 | d2 | d3 | d4 | p8 | d5 | d6 | d7 | d8
 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
A single bit has been flipped in the above example
Recompute parity bits:
P1 is even parity for d1, d2, d4, d5, and d7 (0, 1, 0, 0, 0) = 1
P2 is even parity for d1, d3, d4, d6, d7 (0, 0, 0, 1, 0) = 1 (p2 miscompare)
P4 is even parity for d2, d3, d4 and d8 (1, 0, 0, 1) = 0
P8 is even parity for d5, d6, d7, d8 (0, 1, 0, 1) = 0 (p8 miscompare)
Which bit do P2 and P8 have in common?
P1: d1 d2 d3 d4 d5 d6 d7 d8 (parity OK)
P2: d1 d2 d3 d4 d5 d6 d7 d8 (parity not OK)
P4: d1 d2 d3 d4 d5 d6 d7 d8 (parity OK)
P8: d1 d2 d3 d4 d5 d6 d7 d8 (parity not OK)
Or, P21 and P23 are in error, so set bits 1 and 3 to 1 and other bits to 0 in a binary number: 0000 1010 = 10 which is the bit position of d6.(or 8 + 2)

## Slide 60: Virtual Memory, Virtual Machines
The protection racket
  Page based virtual memory is the basis of process protection
Need process protection if more than one process is running at once
Architecture must allow
  At least a user and OS process mode
  Allow user privilege read only access to some OS info
  Allow processor to switch privilege levels
  Protect memory state of a process from another process
Most popular method is state bits attached to pages
428

## Slide 61: What is Virtual Memory
Like cache, but
  Processor address width determines VM size
  Cache operations are governed by hardware, VM is a property of the operating system
  Main memory is the complete backing store for cache, but the disk file contains more than the backing store for VM pages.
428

## Slide 62: Address translation
429

## Slide 63: Address Translation
Large size of page table means it is paged
Would cause a double-time hit
  One to get the page of the page table
  A second to get the data from the page
TLB holds parts of the page table and leverages locality to speed address translation
If all worked perfectly, we’d be done
428

## Slide 64: Address translation
430

## Slide 65: The four cache questions
Where can a block (page) be placed in memory?
  In principle, anywhere, main memory is seen as fully associative in regard to pages
How is a block found in main memory?
  The page table and the Translation Lookaside Buffer
What block should be replaced, if needed?
  Same as cache--LRU
What happens on a write?
  Typically write-back
431

## Slide 66: Translation Looksaside Buffer
438

## Slide 67
Putting Cache and Virtual Memory Together
441
This cache is physically indexed and tagged
Cache is hardware
Virtual memory is software

## Slide 68: Combination of Hits and Misses
443

## Slide 69: Implementing Protection
Processor has two modes, user and kernel
Operating system manages virtual memory with kernel-level instructions and calls
A context switch isolates one process’s page table from another process’s
444

## Slide 70: Virtual Memory in MIPS
These are the MIPS registers used to handle virtual memory
Page faults are restartable exceptions
448

## Slide 71: MIPS TLB Miss Handler
Context and EntryLo are Coprocessor 0 registers shown on previous slide
Mfc0, mtc0 and eret are legal instructions in MARS, but the C0 registers are not all there
Tlbwr is a kernel-privilege instruction only (not supported by MARS)
449

## Slide 72: Virtual Memory Summary
Pages are large (4K) compared to cache block sizes
Must map between virtual addresses and physical addresses
Main memory handles pages in fully associative fashion
LRU important replacement strategy since page faults take a long time to service
452

## Slide 73: Thrashing
When main memory is small and page faults are frequent
Belady’s anomaly
  Increasing main-memory size leads to more page faults
  From early virtual memory schemes which didn’t use LRU replacement strategy
453

## Slide 74: Common Framework for Cache and Virtual Memory
Where can block be placed?
How is it found again?
Which block should be replaced on a miss?
How are writes different?
454

## Slide 75: The Three C’s for Misses
Compulsory
  On first-ever access
Capacity
  No room
Conflict
  Room, but not in the set
459

## Slide 76: Overall Miss Rate vs Cache Size
460

## Slide 77: Fixes and Their Drawbacks
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to pollution.
461

## Slide 78: Say We Want to Design a Cache Controller
Requirements
  Direct-mapped
  Write-back using write allocate
  Block size is 16 bytes (Block index = 4 bits)
  Cache size is 16 KB (Set index = 10 bits)
  32-byte addresses
  Valid bit and dirty bit per block
  Therefore cache tag is 18 bits
462

## Slide 79: Data Lines
Requirements
  1-bit Read or Write signal
  1-bit Valid signal, saying whether there is a cache operation or not
  32-bit address
  32-bit data from processor to cache
  32-bit data from cache to processor
  1-bit Ready signal, saying the cache operation is complete
462

## Slide 80: General Controller Circuit
464
From CPU and memory
To CPU and memory

## Slide 81: Final State Machine
465
Read or Write Hit
Read or Write Miss
Invalid block available
Or evicted block clean
Read or Write Miss
Invalid block dirty

## Slide 82: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access

## Slide 83: Cache Controller FSM
Could partition into separate states to reduce clock cycle time
465

## Slide 84: Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later)  read returns written value
    c.f. CPU B reading X after step 3 in example
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X
466

## Slide 85: Cache Coherence Problem
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1
467

## Slide 86: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes
Directory-based protocols
  Caches and memory record sharing status of blocks in a directory
468

## Slide 87: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache misses
    Owning cache supplies updated value
CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
 |  |  |  | 0
CPU A reads X | Cache miss for X | 0 (shared) |  | 0
CPU B reads X | Cache miss for X | 0 (shared) | 0 (shared) | 0
CPU A writes 1 to X | Invalidate for X | 1(modify) | (invalidate) | 0
CPU B read X | Cache miss for X | 1 (shared) | 1 (shared) | 1
469

## Slide 88: Multilevel On-Chip Caches
§5.10 Real Stuff: The AMD Opteron X4 and Intel Nehalem
Per core: 32KB L1 I-cache, 32KB L1 D-cache, 512KB L2 cache
Intel Nehalem 4-core processor

## Slide 89: A-8 vs i7
471

## Slide 90: A-8 vs i7 Caches
472
A9 also has only 2 levels

## Slide 91: Memory Performance: A-8
474

## Slide 92: Memory Performance: i7
475

## Slide 93: DGEMM Matrix Multiply Optimizations
x
=
Basic concept:
But cache use is very unoptimized
Instead, break problem into sub-problems
476

## Slide 94: Optimization Comparisons
477